## Slide 1
QuantumRed QR
Thermal imaging module for observation
Thermal imaging cameras are less affected by the weather
than general daytime cameras, and can collect observation data
even at night when there is no light.
Key Features
QVGA (320x240) resolution, 30Hz/60Hz
Provides various interfaces such as USB, MIPI, CameraLink, etc.
Use in various fields such as industrial, transportation, ITS, and smart city
Accurate temperature
Measurement and
High quality imaging
Supports various video
Formats for multiple
applications
Low cost, space free,
comfortable,
easy installation
Accuracy
Expandability
Efficiency

## Slide 2
QuantumRed QR Module Technical Specifications
Mechanical
Imaging
Sensor Technology | Uncooled Microbolometer
Array Format | QVGA(320X240)
Pixel Pitch | 12 µm
Spectral Range | LWIR 8~14 µm
Thermal Sensitivity (NETD) | <40mK(Premium), <50mK(Industrial), <60mK(General)
Frame Rate | 30Hz/60Hz (EL free)
Shutter | With shutter
Accuracy | N/A
Scene Temp. Range | N/A
Size (mm) | 33.0(W) x 33.0(H) x 24.3(D) without lens / interface Board
Weight | 55g (without lens)
Electrical
Environmental
FOV | 11.5° / 28° / 36° / 42° / 50° / 54.4° / custom
Input Voltage | 5.0V
Power Consumption | 1.2W (without Interface Board)
Video Channel | LVCMOS(12/14bit), BT656, BT1120
 | USB(UVC format), Camera-Link(LVDS format), MIPI(CSI-2 format), Analog, Ethernet
Operating Temp. | -40℃ ~ +80℃
Storage Temp. | -40℃ ~ +85℃
Lens
QuantumRed Part Numbering
1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 | 
Main Purpose |  | Resolution |  | Frame/Sec |  | Lens |  | HFOV |  | Grade |  | Temp. Range |  | Interface option | 
Type | Mark | Type | Mark | Type | Mark | Type | Mark | Type | Mark | Type | Mark | Type | Mark | Type | Mark
Surveillance (Military) | MS | 320*240 | 320A | 30Hz | 3 | Yes | L | 5.9° | 059 | < 40mK | P (Premium) | N/A | 000 | USB | U
 |  |  |  |  |  |  |  | 12.5° | 125 |  |  |  |  |  | 
Surveillance | QS |  |  | 60Hz | 6 | No | X | 17.4° | 174 | < 50mK | I (Industrial) |  |  | Camera-Link | C
 |  |  |  |  |  |  |  | 22.8° | 228 |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 32° | 320 | < 60mK | G (General) |  |  | MIPI | M
 |  |  |  |  |  |  |  | 61.1° | 611 |  |  |  |  |  | 
 |  |  |  |  |  |  |  | 75° | 750 |  |  |  |  | Analog | A
 |  |  |  |  |  |  |  | Custom | 000 |  |  |  |  |  | 
 |  |  |  |  |  |  |  |  |  |  |  |  |  | Ethernet | E
 |  |  |  |  |  |  |  |  |  |  |  |  |  | None | N
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
QS | 320A | 3 | L | 059 | I | 000 | U
Part Numbering Sample : QS320A3L059I000U

## Slide 3
QuantumRed QR Module Dimensions
Base Module Dimension
USB Interface Dimension
Camera-Link Interface Dimension